## Slide 1
Car
Base Station
Telemetry Monitor
Status Row
History
Table
Comm
Interface
Comm
Interface
Status Row
History
Table
Management Console
Other Applications
Applications
subscribe to
be notified
of changes
Either told by monitor
of from DB that data has changed
The two interfaces maintain an
on-going connection and the car
passes the contents of the status row
as it changes.
Base station side ACKs each message
and car interface updates history row
to indicate data has been sent
On a re-connect, any un-transmitted
rows are sent to the base station before
status rows are sent.

## Slide 2: Communications Interfaces
Car side should be considered the server.
  On startup, start listening on a port.
  Port should be >1023 so it does not conflict with well-know ports
Connection protocol should follow something similar to the SMTP protocol to allow easy debugging using tools like telnet
Connection setup should include an authentication stage and a version check

## Slide 3: Communications Protocol
ASCII clear-text
Numbers also as ASCII values
Each message requires an answer from the other side
Connection start
  Base Station: HELLO
  Car: NUSOLAR SCx
  Base Station: USER: <some well known name>
  Car: OK or UNAUTHORZED
  Base Station: VERSION 1.0
  Car: OK or INVALID VERSION
This is done to ensure software at the same revision level and that a rouge connection is not accepted since the network will be wide-area and generally open

## Slide 4: Communication Protocol
Command verbs supported by Car
  PAUSE
    Stop notifying base station of data changes. Car should continue to buffer the data
    Car response OK or some error code
  RESUME
    Resume sending data changes
    Car response OK or some error code
  PURGE
    Clear all saved data
    Car response OK or some error code
  SENDALL <starting log entry number>
    Send all data starting with the specified log entry number
    If not specified, then all data in history table is sent

## Slide 5: Communications Protocol
Message format for sending data from car to base station
  DATA,<column count>,<telemetry data>
    <column count> is the number of data columns in <telemetry data>
    <telemetry data> is , separated ascii values
  Base Station responds with OK or some error code

## Slide 6: Car Communications Interface
On startup
  Opens database
  Starts listening on TCP port
  Waits for a mutex set by telemetry logging process or command from base station
  When mutex is set and there is a TCP connection
    For each history record not sent
      Send to base station
      If ACKed, mark as sent, else resend
    Wait on mutex

## Slide 7: Base Station Communications Interface
On startup
  Opens database
  Attempts to establish communications with car
  Starts listening on a TCP port to accept connections from applications that want to be notified of telemetry data changes and that may want to send commands to car
  Waits on receipt of data from car or command from registered listens
  When data is received from car
    Data is saved to database
    Registered listeners are notified via TCP message that includes the <telemetry data> portion of the message

## Slide 8: Base Station Applications
On startup
  Open connection to database
  Open connection to base station communications interface for notification of changes
When data change notification is received, do what ever makes sense for the application